Slide 4
- To simplify the path explored, final orientation input is not required
- (RPM1, RPM2) – can be 2 arbitrary values inputted by user
  - Revelations per Minute
  - Clearance initially in mm, will convert to cm for plotting and back to meters for Gazebo

Slide 5
- TurtleBot3 Data Sheet Link: https://emanual.robotis.com/docs/en/platform/turtlebot3/features/
- Wheel Radius = 66mm/2 = 33mm
- Robot Radius = 105 mm
  - Robot Radius need to be added to user inputted clearance value to create obstacle map
  - So total clearance is 105 (radius) plus clearance 5 = 110
- Wheel Distance L = 160 mm (distance between centers of wheels)

Slide 6
- 8 Move Action Set, only 2 will result in straight lines as in slide 9
- Action are curves not straight lines

- [0, RPM1] – Turn left at RPM1
- [RPM1, 0] – Turn right at RPM1
- [RPM1, RPM1] – Move forward both wheels with RP1
- [0, RPM2] – Turn left at RPM2
- [RPM2, 0] – Turn right at RPM2
- [RPM2, RPM2] – Move forward both wheels with RP2
- [RPM1, RPM2] – Move both wheels forward, turn right if RPM1 < RPM2, else turn left
- [RPM2, RPM1] – Move both wheels forward, turn left if RPM1 < RPM2, else turn right

Limit of RPM values should be listed in data sheets – rpm1 two rpm2 do not use 10/15, instead use say 10/30 or 10/50

Slide 8

- directly specifies the two angular wheel velocities (e.g., in radians per second).
- Convert between revolutions per minute and radians per second to convert from RPM values to ur and ul
- Let dt = 0.1
- dx: integrate similar to modeling ENPM661 HW# 4 where we integrated the circle equation
  - you know dx and the current x value, so new_x = x + dx
  - Say (x,y) = (0,0)
  - dt = 0.1 means dividng 1 second in different increments of 0.1 seconds
  - robot will end up new location by adding x to dx, y to dy, and theta to theta dx

- Refer to cost.py file to understand cost function logic
  - D – cost value L between every 0.1 seconds from parent to child node (1 second total)
  - Theta is radians
  - C2G is measured as distance between xn,yn and goalx,goaly

Slide 12
- Checking for visited nodes:
- In Project Phase 1, we used visited_matrix but the angles are not restricted to 12 angle values this time or increments of 30 degrees
  - 500x1200x360 is too huge of a matrix
  - Solution: Just compare x and y of current node to search node to determine if search node is visited or not – method 1

Slide 13
Don’t plot curves, just join that node and previous node by single, just draw line between parent and child every 0.1 seconds to make it easier, if I zoom out they look like curves

Slide 14
Use Project Phase 2 Part 2 map for Project 3 Phase 2 Part 1 & 2 – slide 18

Slide 15
- In Phase 1 we were in cm, now project map defined in mm. Convert dimensions to cm by scaling by a 100
- 1pixel is 1cm
- Phase 2 map is 6 meters by 2 meters which is 6 pixels by 2 pixels?
  - Convert everything to cm so 600 cm x 200 m
- when you give inputs to your code, it should respect to 0,0
  - 0,0 maps to → 0.5,1 Mapping
- Before going to Gazebo, convert to meters
  - Convert velocity from cm/s back to m/s

Resources
http://msl.cs.uiuc.edu/planning/node659.html

child_theta = parent_theta + angle_to_add

is_node_duplicate

Enter robot clearance between 0 and 0.2: 0.2
Robot Clearance: 0.2

Enter robot Revolutions per Minute (RPM1) integer value between 10 and 55: 10
Robot RPM1: 10

Enter robot Revolutions per Minute (RPM2) integer value between 10 and 55: 30
Robot RPM2: 30

Enter start node's x coordinate. x coordinate can range from 0 to 299: 65
Enter start node's y coordinate. y coordinate can range from 0 to 99: 45
Enter the orientation of the robot at the start point in degrees: 0
Start node x-coordinate: 65
Start node y-coordinate: 45

Enter goal node's x coordinate. x coordinate can range from 0 to 299: 85
Enter goal node's y coordinate. y coordinate can range from 0 to 99: 45
Goal node x-coordinate: 85
Goal node y-coordinate: 45